## Slide 1
Safe Keypad System
8051 Microcontroller · CTEC 350 · Spring 2026
Dr. Duke

## Slide 2
Why This Matters
Keypad-based access control is one of the most common forms of physical security in the real world — and it all runs on embedded systems exactly like the 8051.
No network needed
Unlike smart card or phone-based systems, a keypad lock works even if the internet is down or infrastructure fails — critical in industrial settings.
Cheap and reliable
A microcontroller-based keypad system can cost a few dollars in hardware. That is why they are everywhere — from safes to server rooms to gate panels.
Embedded systems are everywhere
Most of the devices around us — appliances, cars, medical equipment — run on small microcontrollers like the 8051. Learning to program one directly in assembly is a core skill for any hardware engineer.
Real constraints, real solutions
The 8051 has limited RAM and no operating system. Every decision in this project — using lookup tables, multiplexing the display, scanning the keypad — exists because of those constraints. That is what embedded engineering actually looks like.

## Slide 3
What It Does
A digital safe that accepts a 4-digit combination on a keypad.
Each digit typed appears on the 7-segment display and shifts left — just like an ATM.
Enter the correct code (3-5-7-9) and the display flashes OPEn.
Wrong code does nothing. Press * to clear and try again.
Application
Server rooms, electrical panels, and lab storage use keypad locks because they need no network or smart cards — just a code.
Peripherals
4×4 Matrix Keypad
4-Digit 7-Segment Display

## Slide 4
Hardware
Keypad — P1
Rows P1.0–P1.3 → OUTPUT (driven LOW to scan)
Cols P1.4–P1.7 → INPUT (pulled HIGH)
16 keys using only 8 pins
* = clear key
Display — P2 & P3
Segments a–g → P2 (bit 0 through bit 6)
Digit select → P3.0–P3.3 (active LOW)
Common-cathode, 4 digits
Multiplexed at 250 Hz
Port Map: P1 → Keypad P2 → Segment Data P3 → Digit Select P0 → Unused

## Slide 5
How Keypad Scanning Works
1
Drive one row LOW
Set P1.0 LOW, all other rows HIGH. Activates row 0 for scanning.
2
Read the columns
Read P1.4–P1.7. Any column reading LOW means a key in that row is pressed.
3
Calculate the key
Index = Row × 4 + Column. Row 0, Col 2 → Index 2 → digit 3.
4
Move to next row
Repeat for all 4 rows. Return FFH if nothing found.

## Slide 6
Display Multiplexing
The display only turns on one digit at a time, but cycles through all four so fast — 250 times per second — that your eye sees all four as always lit. This is persistence of vision.
Timer 0 ISR — every 1 ms
1. Blank all digits (prevent ghosting)
2. Get buffer value for current digit
3. Convert to 7-seg pattern via SEG_TABLE
4. Write to P2, enable digit on P3
5. Advance digit index (0→1→2→3→0)
1 ms per digit
× 4 digits
= 4 ms cycle
= 250 Hz refresh

## Slide 7
The Code
SCAN_KEY
Drives each row LOW one at a time, reads column bits, returns key index 0–15 or FFH.
KEY_TO_DIGIT
Converts raw index to digit 0–9 using a MOVC lookup table. Returns FFH for non-digit keys.
DO_STORE
Shifts display buffer left. Stores new digit in rightmost slot. Increments counter.
CHECK_COMBO
Compares each entered digit against S0–S3 (3,5,7,9). Match → flash OPEn. No match → do nothing.
T0_ISR
Timer interrupt every 1 ms. Writes segment data to P2 and enables one digit on P3.
CLEAR_ALL
Resets display buffer, input counter, and key buffer. Called on * key or after correct combo.

## Slide 8
Combination Check
Once 4 digits are entered, CHECK_COMBO compares each one against the secret values stored as constants in code.
Correct (3 – 5 – 7 – 9)
All 4 digits match the constants S0–S3
FLASH_OPEN runs — display shows OPEn
Flashes 3 times, 300 ms on / 300 ms off
CLEAR_ALL resets everything to blank
Incorrect
CJNE instruction jumps to WRONG on any mismatch
WRONG just returns — nothing happens on screen
Display keeps showing the last 4 entered digits
Press * to clear and try again

## Slide 9
Summary
Built a working safe keypad system on the 8051 microcontroller
Two peripherals: 4×4 matrix keypad and multiplexed 7-segment display
Column-scan detects 16 keys with only 8 I/O pins
Timer 0 ISR drives the display at 250 Hz without slowing down the main loop
Secret combination: 3 – 5 – 7 – 9
Thank you